## Slide 1: Week-4
4.3.7 Fast Ethernet
5.2

## Slide 2: What leads to fast Ethernet?
To pump up the speed, various industry groups proposed two new ring based optical LANs.
One was called FDDI and the other was called fiber channel.
Both of them failed for desktop, management was complicated, complex chips and very expensive

## Slide 3: Ethernet
Physical Media :-
  10 Base5 - Thick Co-axial Cable with Bus Topology
  10 Base2 - Thin Co-axial Cable with Bus Topology
  10 BaseT - UTP Cat 3/5 with Tree Topology
  10 BaseFL - Multimode/Singlemode Fiber with Tree
  Topology
Maximum Segment Length
  10 Base5 - 500 m with at most 4 repeaters (Use Bridge to extend the network)
  10 Base2 - 185 m with at most 4 repeaters (Use Bridge to extend the network)
  10 BaseT - 100 m with at most 4 hubs (Use Switch to extend the network)

## Slide 4: Fast Ethernet
100 Mbps bandwidth
Uses same CSMA/CD media access protocol and packet format as in Ethernet.
100BaseTX (UTP) and 100BaseFX (Fiber) standards
Physical media :-
    100 BaseTX - UTP Cat 5e
    100 BaseFX - Multimode / Singlemode Fiber
Full Duplex/Half Duplex operations.

## Slide 5: Fast Ethernet
Provision for Auto-Negotiation of media speed: 10 Mbps or 100Mbps (popularly available for copper media only).
Maximum Segment Length
    100 Base TX - 100 m
    100 Base FX - 2 Km (Multimode Fiber)
    100 Base FX - 20 km (Singlemode Fiber)

## Slide 6: Gigabit Ethernet
1 Gbps bandwidth.
Uses same CSMA/CD media access protocol as in Ethernet and is backward compatible (10/100/100 modules are available).
1000BaseT (UTP), 1000BaseSX (Multimode Fiber) and 1000BaseLX (Multimode/Singlemode Fiber) standards.
Maximum Segment Length
    1000 Base T - 100m (Cat 5e/6)
    1000 Base SX - 275 m (Multimode Fiber)
    1000 Base LX - 512 m (Multimode Fiber)
    1000 Base LX - 20 Km (Singlemode Fiber)
    1000 Base LH - 80 Km (Singlemode Fiber)

## Slide 7: Routing Algorithm
Part of N/L
Decides 2 things:
  Which i/p pkt to transmit?
  Where/Which o/p line to select?
Session routing: for the whole session no need to change the output line selected by 1st packet
In general routers have 2 phase:
  Forwarding
  Table updating

## Slide 8: Non-adaptive & adaptive algorithm
Routing algorithm can be grouped into:
  Non-adaptive algorithms (fixed traffic light)
    do not base their routing decisions on measurements or estimates of the current traffic and topology.
    Instead, the choice of the route to use to get from I to J (for all I and J)is computed in advance, off-line, and downloaded to the routers when the network is booted.
    This procedure is sometimes called static routing.

## Slide 9
  Adaptive algorithms
  change their routing decisions to reflect changes in the topology, and usually the traffic as well.
  Adaptive algorithms differ in where they get their
    information (e.g., locally, from adjacent routers, or from all routers),
    when they change the routes (e.g., every ∆T sec, when the load changes or when the topology changes), and
    What metric is used for optimization (e.g., distance, number of hops, or estimated transit time).

## Slide 10: The Optimality Principle
the optimality principle and the sink tree provide a benchmark against which other routing algorithms can be measured.
  a general statement about optimal routes without regard to network topology or traffic
  It states that if router J is on the optimal path from router I to router K, then the optimal path from J to K also falls along the same route.

## Slide 11
Where the distance metric is the number of hops.
Sink tree is not necessarily unique; other trees with the same path lengths may exist.
The goal of all routing algorithms is to discover and use the sink trees for all routers.

## Slide 12
Design Goals of Routing Algorithms
  Algorithm Types
  Routing Metrics
  Dynamic Routing Algorithms

## Slide 13: Algorithm types
Static Vs Dynamic
Single Path Vs Multiple Path
Host Intelligent Vs Router Intelligent
Intradomain Vs Interdomain

## Slide 14: Routing Metrics
Path Length
Reliability
Delay
Bandwidth
Load
Communication cost

## Slide 15: Static Algorithms
  Shortest Path Algorithm
  Flooding
  Flow based Routing
Dynamic Algorithms
  Distance Vector Routing
  Link State Routing
  Hierarchical Routing

## Slide 16
Given a network topology and a set of weights describing the cost to send data across each link in the network
Find the shortest path from a specified source to all other destinations in the network.
Shortest path algorithm first developed by E. W. Dijkstra
Shortest Path Routing (a non-adaptive routing algorithm)

## Slide 17
Mark the source node as permanent.
Designate the source node as the working node.
Set the tentative distance to all other nodes to infinity.
While some nodes are not marked permanent
Compute the tentative distance from the source to all nodes adjacent to the working node. If this is shorter than the current tentative distance replace the tentative distance of the destination and record the label of the working node there.
Examine ALL tentatively labeled nodes in the graph. Select the node with the smallest value and make it the new working node. Designate the node permanent.

## Slide 18: Example of Shortest Path Routing

## Slide 19: Flooding (a nonadaptive routing algorithm)
Brute force routing
  Every incoming packet is sent on every outgoing line
  Always finds the shortest path quickly
  Also finds many long paths
  Time to live is set to size of subnet
Selective Flooding
  Flood only in the direction of the destination
Practical in a few settings
  Military Applications
  Distributed Databases
  Metric for comparison

## Slide 20: Distance Vector Routing (an adaptive routing algorithm)
Bellman-Ford Routing
Ford Fulkerson Algorithm
Original ARPANET routing algorithm
Previously used on Internet (RIP)
Early version of DecNet and Novell’s IPX
AppleTalk and Cisco routers use improved versions of this algorithm

## Slide 21: Distance Vector Routing (an adaptive routing algorithm)
Neighboring routers periodically exchange information from their routing tables.
Routers replace routes in their own routing tables anytime that neighbors have found better routes.
Information provided from neighbors
  Outgoing line used for destination
  Estimate of time or distance
    can be number of hops, time delay, packet queue length, etc.

## Slide 22: Distance Vector Routing (an adaptive routing algorithm)

## Slide 23: Distance Vector Routing (an adaptive routing algorithm)

## Slide 24: The Count to Infinity Problem

## Slide 25: Link State Routing (an adaptive routing algorithm)
Five Steps
1.) Discover your neighbors and learn their addresses.
2.) Measure the cost (delay) to each neighbor.
3.) Construct a packet containing all this information
4.) Send this packet to all other routers.
5.) Compute the shortest path to every other router.
Send “Hello” packet on each point-to-point line. Destination node replies with its address.
1.) Discovering Your Neighbors

## Slide 26: 2.) Measuring Line Cost
Send an “ECHO” packet over the line.
Destination is required to respond to “ECHO” packet immediately.
Measure the time required for this operation.
Question: Should we measure just the time it takes to transmit the packet, or should we include the time that the packet waits in the queue?

## Slide 27: Argument 2:
We should include the time that the packet spends in the queue, as this provides a more accurate picture of the real delays.
We should only include the transmission times, otherwise the network is likely to oscillate between preferred paths.

## Slide 29: Build Link State Packets
Building the link state packets is easy.
when to build? 1) periodically, and
2) when some significant event occurs,

## Slide 30: Distributing the Link State Packets
Use selective flooding
Sequence numbers prevent duplicate packets from being propagated
Lower sequence numbers are rejected as obsolete
Dijkstra’s Shortest Path algorithm is used to determine the shortest path to each destination.
Computing the New Routes

## Slide 31: Internetworking
More networks are connected to form internet

## Slide 32
The purpose of interconnecting all these networks is to allow users on any of them to Communicate with users on all the other ones and also to allow users on any of them to access data on any of them.

## Slide 33: How Networks Differ

## Slide 34: How Networks Can Be Connected?
Repeaters or Hubs (which layer?)
Bridges and Switches. (?)
  Can translate protocol from Ethernet to FDDI or to 802.11. (minor protocol translation)
Routers (?)
  A router that can handle multiple protocols is called a multiprotocol router.

## Slide 35: Switch vs Router
Switch only checks MAC address, but
Router checks the IP address.

## Slide 37: Tunneling

## Slide 38: Fragmentation. Why?
1. Hardware (e.g., the size of an Ethernet frame).
2. Operating system (e.g., all buffers are 512 bytes).
3. Protocols (e.g., the number of bitsin the packet length field).
4. Compliance with some (inter)national standard.
5. Desire to reduce error-induced retransmissions to some level.
6. Desire to prevent one packet fromoccupying the channel too long.

## Slide 39: IP Fragmentation
Every Network has Own Maximum Transmission Unit (MTU)
  Largest IP datagram it can carry within its own packet frame
    E.g., Ethernet is 1500 bytes
  Don’t know MTUs of all intermediate networks in advance
IP Solution
  When hit network with small MTU, fragment packets
    Might get further fragmentation as proceed farther
host
host
router
router
MTU = 4000
MTU = 1500
MTU = 2000

## Slide 40: Fragmentation Related Fields
Length
  Length of IP fragment
Identification
  To match up with other fragments
Fragment offset
  Where this fragment lies in entire IP datagram
Flags
  “More fragments” flag
  “Don’t fragment” flag

## Slide 41: Fragmentation Related Fields
Length
  Length of IP fragment
Identification
  To match up with other fragments
Fragment offset
  Where this fragment lies in entire IP datagram
Flags
  “More fragments” flag
  “Don’t fragment” flag

## Slide 42: IP Fragmentation Example #1
host
router
MTU = 4000
IP
Header
IP
Data
Length = 3820, M=0

## Slide 43: IP Fragmentation Example #2
router
router
MTU = 2000
IP
Header
IP
Data
Length = 3820, M=0
3800 bytes
IP
Header
IP
Data
Length = 2000, M=1, Offset = 0
1980 bytes
IP
Data
IP
Header
Length = 1840, M=0, Offset = 1980
1820 bytes
IP Header= 20 bytes

## Slide 44: IP Fragmentation Example #3
IP
Header
IP
Data
Length = 2000, M=1, Offset = 0
1980 bytes
IP
Data
IP
Header
Length = 1840, M=0, Offset = 1980
1820 bytes
host
router
MTU = 1500
IP
Header
IP
Data
Length = 1500, M=1, Offset = 0
1480 bytes
IP
Header
IP
Data
Length = 520, M=1, Offset = 1480
500 bytes
IP
Header
IP
Data
Length = 1500, M=1, Offset = 1980
1480 bytes
IP
Header
IP
Data
Length = 360, M=0, Offset = 3460
340 bytes

## Slide 45: IP Reassembly
Fragments might arrive out-of-order
  Don’t know how much memory required until receive final fragment
Some fragments may never arrive
  After a while, give up entire process
IP
Header
IP
Data
Length = 1500, M=1, Offset = 0
IP
Header
IP
Data
Length = 520, M=1, Offset = 1480
IP
Header
IP
Data
Length = 1500, M=1, Offset = 1980
IP
Header
IP
Data
Length = 360, M=0, Offset = 3460
IP
Data
IP
Data
IP
Data
IP
Data