## Slide 1: Week-1
Instructor: D.MSI
https://sites.google.com/site/drmohammadshahidulislam

## Slide 2: Computer Networks 1.5 hours in a week, 3.00 Cr.
Dr. Mohammad Shahidul Islam
Associate Professor

## Slide 3: Reference Book(s):
1. Computer Networks - Andrew S. Tanenbaum
2. Computer Networks: Protocols, Standards, and Interfaces - Uyless Black
3. Internetworking with TCP/IP: Principles, Protocols, Architecture - D. E. Comer
4. TCP/IP Illustrated Vol. I - W. R. Stevens

## Slide 4: Course Contents:
Protocol hierarchies; Data link control: HDLC;
DLL in Internet; DLL of ATM; LAN Protocols: Standards IEEE 802;
Hubs, Bridges, and Switches, FDDI,
Fast Ethernet; Routing Algorithm;
Internetworking, WAN; Fragmentation; Firewalls;
IPV4, IPV6, ARP, RARP, Mobile IP,
Network layer of ATM;
Transport Protocols; Transmission Control Protocol: Connection Management,

## Slide 5: Course Contents:
Transmission Policy, Congestion Control, Timer Management;
UDP; AAL of ATM; wireless networks,
mobile computing, and high speed networks;
Gigabit Ethernet; Domain Name System: Name servers;
Email and Its privacy; SNMP; HTTP;
World Wide Web; Network security: Cryptography,
DES, IDEA, public key algorithm;
Authentication; Digital signatures.

## Slide 6: Today
Computer Network basics
Protocol hierarchies;
Data link control: HDLC;

## Slide 7: Computer Networks
Define?
Computer network connects two or more autonomous computers.
The computers can be geographically located anywhere.
Introduction to Computer Networks

## Slide 8: LAN, MAN & WAN
Network in small geographical Area (Room, Building or a Campus) is called LAN (Local Area Network)
Network in a City is call MAN (Metropolitan Area Network)
Network spread geographically (Country or across Globe) is called WAN (Wide Area Network)
Introduction to Computer Networks

## Slide 9: Applications of Networks
Resource Sharing
  Hardware (computing resources, disks, printers)
  Software (application software)
Information Sharing
  Easy accessibility from anywhere (files, databases)
  Search Capability (WWW)
Communication
  Email
  Message broadcast
Remote computing
Distributed processing (GRID Computing)
Introduction to Computer Networks

## Slide 10: Network Topology BSRM
The network topology defines the way in which computers, printers, and other devices are connected.
A network topology describes the layout of the wire and devices as well as the paths used by data transmissions.
Introduction to Computer Networks

## Slide 11: Bus Topology
Commonly referred to as a linear bus, all the devices on a bus topology are connected by one single cable.

## Slide 12: Star & Tree Topology
The star topology is the most commonly used architecture in Ethernet LANs.
When installed, the star topology resembles spokes in a bicycle wheel.
Larger networks use the extended star topology also called tree topology. When used with network devices that filter frames or packets, like bridges, switches, and routers, this topology significantly reduces the traffic on the wires by sending packets only to the wires of the destination host.
Introduction to Computer Networks

## Slide 13: Ring Topology
A frame travels around the ring, stopping at each node. If a node wants to transmit data, it adds the data as well as the destination address to the frame.
The frame then continues around the ring until it finds the destination node, which takes the data out of the frame.
  Single ring – All the devices on the network share a single cable
  Dual ring – The dual ring topology allows data to be sent in both directions.
Introduction to Computer Networks

## Slide 14: Mesh Topology
The mesh topology connects all devices (nodes) to each other for redundancy and fault tolerance.
It is used in WANs to interconnect LANs and for mission critical networks like those used by banks and financial institutions.
Implementing the mesh topology is expensive and difficult.

## Slide 15: Network Components
Physical Media
Interconnecting Devices
Computers
Networking Software
Applications
Introduction to Computer Networks

## Slide 16: Networking Media
Networking media can be defined simply as the means by which signals (data) are sent from one computer to another (either by cable or wireless means).
Introduction to Computer Networks

## Slide 17: Networking Devices
HUB, Switches, Routers, Wireless Access Points, Modems etc.
Introduction to Computer Networks

## Slide 18: Computers: Clients and Servers
In a client/server network arrangement, network services are located in a dedicated computer whose only function is to respond to the requests of clients.
The server contains the file, print, application, security, and other services in a central computer that is continuously available to respond to client requests.
Introduction to Computer Networks

## Slide 19: Networking Protocol: TCP/IP

## Slide 20: Applications
E-mail
Searchable Data (Web Sites)
E-Commerce
News Groups
Internet Telephony (VoIP)
Video Conferencing
Chat Groups
Instant Messengers
Internet Radio
Introduction to Computer Networks

## Slide 21: Protocol Hierarchies
• Most networks are organized as a series of layers or levels
– Each layer offers certain services to the higher layers
• Protocol
– an agreement between the communicating parties on how communication is to proceed.
– Layer n protocol

## Slide 22
Fig: protocols, layers and interfaces

## Slide 23: Peers and Interfaces
• Peers
– The entities comprising the corresponding layers on different machines
• Interface
– between each pair of adjacent layers
– defines which primitive operations and services the lower layer offers to the upper one.

## Slide 24: Entities and Peer Entities
• An entity
– an active element in a layer
– can be a software entity (a process), a hardware entity (an I/O chip), or both (an I/O chip with its driver).
• Peer entities
– entities in the same layer on different machines

## Slide 25: Protocol Stacks
• A protocol stack.
– A list of protocols used by a certain system, one protocol per layer
• Network architecture
– A set of layers and protocols

## Slide 26: Layers at An Interface

## Slide 27: Example: SAPs in LLC

## Slide 28: Till Now
LAN, MAN & WAN
Applications of Networks
Network Topology BSRM
Network Components PINCONA
:protocols, layers and interfaces
Peers, Entities and Peer Entities
Protocol Stacks
Layers at An Interface
Connections Multiplexing

## Slide 29: Connections Multiplexing
Upward Multiplexing: Several layer N connections should be multiplexed into a
layer N-1 connection.
Downward Multiplexing: a layer N connection uses several layer N-1 connections.

## Slide 30: Connections Multiplexing[p-510-511]

## Slide 31: Connection-Oriented and Connectionless Services
• connection-oriented
– Establish a connection first, use the
connection, and then release the connection.
– Example: the telephone system
• connectionless
– No connection is established.
– Example: the postal system

## Slide 32: Service Primitives
• Request
– layer n+1 to layer n
• Indication
– layer n to layer n+1
– signal an event
• Response
– layer n+1 to layer n
– respond to the previous
indication
• Confirm
– layer n to layer n+1
– confirm the previous request

## Slide 33: Reference Models
• The OSI Reference Model
– based on a proposal developed by the
International Standards Organization (ISO)
– a first step toward international
standardization of the protocols used in the
various layers.
• The TCP/IP Reference Model

## Slide 34: The OSI Reference Model

## Slide 35: The TCP/IP Reference Model

## Slide 36: Physical Layer
- main function to transmit bits over a communication channel
- to establish and terminate a connection to a communications medium
- responsible to make sure that when one side sends a '1' bit the other side will receive '1' bit and not '0' bit.

## Slide 37: Data Link Layer
provides means to transfer data between network entities.
- it takes the bit streams of data from the Network Layer
- breaks into frames and passes them to the physical layer.
- At the receiving end data link layer detects and possibly corrects the errors
- passes the correct stream to the network layer.
- also concerned with flow control techniques.

## Slide 38: Network Layer
- performs network routing,
- flow control
- error control functions.
- prevents the possibility of congestion .

## Slide 39: Transport Layer
-main task to accept data from the Session layer,
- split them up into smaller units
- passes them to the Network layer
- make sure that all the pieces arrived correctly.
- checks the sequence of packets.

## Slide 40: Session Layer
responsible for controlling exchange information and
sets up, coordinates, and terminates conversations, exchanges, and dialogs between the applications at each end
synchronization.
Provides a session
SS

## Slide 41: Presentation Layer
Responsible to translate different data formats from the representation used inside the computer (ASCII) to the network standard representation and back.
Computers use different codes for representing character strings so a standard encoding must be used and is handled by the presentation layer.
Generally in a few words this layer is concerned with the syntax and semantics of the information transmitted.
PS

## Slide 42: Application layer
Makes sure that the other party is identified and can be reached
If appropriate, authenticates either the message sender or receiver or both
Makes sure that necessary communication resources exist (for example, is there a modem in the sender's computer?)
Ensures agreement at both ends about error recovery procedures, data integrity, and privacy
Determines protocol and data syntax rules at the application level

## Slide 43: Example Data Link Protocols
HDLC – High-Level Data Link Control
The Data Link Layer in the Internet

## Slide 44: High-Level Data Link Control
Frame format for bit-oriented protocols
All HDLC frames begin with the HDLC flag 01111110, which is byte stuffed if occurs in the rest of the frame.
The address field : on lines with multiple terminals, the address field is used to identify one of the terminals
The control field: used for sequence numbers, acknowledgements and other purposes.
The data field: may contain any information. It can have any length, although the efficiency of the checksum falls down with increasing frame length, due to the probability of occurrence of multiple burst errors.
CRC – checksum obtained with techniques………
End of frame (same as start of frame)
Notes: The frame begins with a frame sequence: 01111110
The address field : on lines with multiple terminals, the address field is used to identify one of the terminals
The control field: used for sequence numbers, acknowledgements and other purposes as shown on the next slide
The data field: may contain any information. It can have any length, although the efficiency of the checksum falls down with increasing frame length, due to the probability of occurrence of multiple burst errors.
The Checksum is the Cyclic Redundancy Code obtained with the technique described earlier
The frame is ended with another frame sequence: 01111110

## Slide 45: High-Level Data Link Control (2)
Control field of
(a) An information frame.
(b) A supervisory frame.
(c) An unnumbered frame.
Notes: There are three types of frames: information, supervisory and unnumbered.

## Slide 46: Information Frame
SEQ – 3 bits sequence numbers are used
NEXT – used for piggybacking acknowledge
  All of the HDLC protocols adhere to the convention that instead of sending the sequence number for the frame that has been received correctly, the acknowledgement contains the sequence number of the next frame that is expected (not received yet).
Notes: The protocol is using a sliding window with 3 bits sequence numbers. Up to 7 unacknowledged frames can be in the traffic at any time. The SEQ field is the frame sequence number, while the NEXT field is the piggyback acknowledgement.
All of the HDLC protocols adhere to the convention that instead of sending the sequence number for the frame that has been received correctly, the acknowledgement contains the sequence number of the next frame that is expected (not received yet).
The P/F bit stands for Pool/Final and it is used when a computer is polling a group of terminals. When used as P, the computer is inviting the terminals to send data. All the frames from the terminal, except the final one, have the P/F flag set to P. The final one is F. The F flag is sometimes used to force the other machine to send a supervisory frame immediately, without waiting for reverse traffic where to piggyback the window information.

## Slide 47: Information Frame
The P/F bit stands for Pool/Final and it is used when a computer is polling a group of terminals.
  When used as P, the computer is inviting the terminals to send data. All the frames from the terminal, except the final one, have the P/F flag set to P. The final one is F.
  The F flag is sometimes used to force the other machine to send a supervisory frame immediately, without waiting for reverse traffic where to piggyback the window information.
Notes: The protocol is using a sliding window with 3 bits sequence numbers. Up to 7 unacknowledged frames can be in the traffic at any time. The SEQ field is the frame sequence number, while the NEXT field is the piggyback acknowledgement.
All of the HDLC protocols adhere to the convention that instead of sending the sequence number for the frame that has been received correctly, the acknowledgement contains the sequence number of the next frame that is expected (not received yet).
The P/F bit stands for Pool/Final and it is used when a computer is polling a group of terminals. When used as P, the computer is inviting the terminals to send data. All the frames from the terminal, except the final one, have the P/F flag set to P. The final one is F. The F flag is sometimes used to force the other machine to send a supervisory frame immediately, without waiting for reverse traffic where to piggyback the window information.

## Slide 48: Supervisory Frame
Various kinds of SUPERVISORY frames are distinguished by the type filed:
  [00]Type 0 is an acknowledgement frame (called RECEIVE READY), used to indicate the next frame expected
  [01]Type 1 is a negative acknowledgement frame (called REJECT), used to indicate an error. The NEXT field indicates the first frame in sequence that has not been received correctly. The sender is requested to send all frames beginning at NEXT
Notes: Various kinds of SUPERVISORY frames are distinguished by the type filed:
  Type 0 is an acknowledgement frame (called RECEIVE READY), used to indicate the next frame expected
  Type 1 is a negative acknowledgement frame (called REJECT), used to indicate an error. The NEXT field indicates the first frame in sequence that has not been received correctly. The sender is requested to send all frames beginning at NEXT
  Type 2 is RECEIVE NOT READY. It acknowledges all frames up to but not including the NEXT one. It also tells the sender to stop sending. When the receiver is ready again, it sends a RECEIVE READY.
  Type 3 is a SELECTIVE REJECT. It calls for retransmission of only the frame specified. Thus, if a receiver wants to buffer out of sequence frames, it can force the retransmission of a specific frame by using a selective reject.

## Slide 49: Supervisory Frame
  [10]Type 2 is RECEIVE NOT READY. It acknowledges all frames up to but not including the NEXT one. It also tells the sender to stop sending. When the receiver is ready again, it sends a RECEIVE READY.
  [11]Type 3 is a SELECTIVE REJECT. It calls for retransmission of only the frame specified. Thus, if a receiver wants to buffer out of sequence frames, it can force the retransmission of a specific frame by using a selective reject.

## Slide 50: Unnumbered Frame
UNNUMBERED FRAME is used for control and to carry data when unreliable connectionless service is required.
Using this frame, a number of commands can be sent:
  DISConect – allows a machine to announce its intention to bring down the connection
  SABM (Set Asynchronous Balanced Mode) – resets the line
  FRMR (Frame Reject) – indicates that a frame with correct checksum but incorrect semantics has arrived
More control frames are actually available for initialization, polling and status reporting.